Linux tmpfs
Mark Veltzer
mark@veltzer.net

---
tmpfs intro
- tmpfs is a linux filesystem that stores all of your files in RAM.
- Available in all recent linux versions.
- Is used by some distributions by default for some folders (/tmp, /dev, /var/run, /run).
- You can mount your own folders as tmpfs, but need root or CAP_SYS_ADMIN to do so.
- Or you can just have a per-prepared tmpfs already defined in /etc/fstab.

---
tmpfs read(2) performance
- tmpfs offers some performance benefits for read and write operations.
- Actually the read difference between tmpfs and regular file system is not that great and is centered around the first time you read a certain area of a file.
- In tmpfs this, and all subsequent reads, will be a memcpy.

---
tmpfs read performance (cont)
- In a regular disk based file system the first read will be slow while subsequent reads will probably be from the OS page cache and so will resolve to memcpy.
- But in tmpfs you are guaranteed to get memcpy performance on both first and all subsequent reads.
- And you can control the maximum size of your tmpfs filesystem.

---
tmpfs write performance
- Write performance in tmpfs is always just a memcpy to the kernel (if you have enough space that is...)
- And you don't apply any pressure on any real disk file system that you have running in parallel and used by other programs.
- But the downside is that you data never reaches any persistent storage...

---
tmpfs disadvantages
- When your system crashes (power failure, OS bug, hardware failure, whatever) you lose your tmpfs data.
- This is unlike disk based file systems where you can guarantee your data will be there by calling fsync, fdatasync, sync, sync_file_range.
- tmpfs also lacks some advanced file system features (compression and others).

---
When should you use tmpfs?
- You should use tmpfs for faster access to data which is not critical.
- Much like a memory cache.
- Actually it's better to use some in process memory cache which will be more effective because accessing it does not require system calls.
- On the other hand you could mmap tmpfs files.

---
Using tmpfs
- First make a folder:
  mkdir -p /mnt/tmp
- Then mount it:
  mount -t tmpfs -o size=20m tmpfs /mnt/tmp

---
References
- http://www.thegeekstuff.com/2008/11/overview-of-ramfs-and-tmpfs-on-linux/
- http://www.linux-mag.com/id/7689/
- http://en.wikipedia.org/wiki/Tmpfs
- http://www.ibm.com/developerworks/library/l-fs3/index.html
- http://fixunix.com/linux/1717-tmpfs-swap.html