GCC on Linux
The beast and it's taming
Mark Veltzer
mark.veltzer@gmail.com

---
Getting data from stdin
- Input file would be -
- You have to specify the input language using the -x flag
- Possible values include: c,c++,objective-c,objective-c++,assembler,assembler-with-cpp,ada,f77,f95,java and many more
- Example: gcc -x c -
- Output file either specified with -o or would be the standard (a.out).

---
Getting help
- man gcc – good for quick reference to flags
- Info gcc – more in depth (warning: entire book!)
- gcc – help – only most common flags but good for 99% of the cases (two minuses!)
- gcc –target-help – shows options that have to do with target code generation
- gcc –help=warnings – shows all warning flags

---
What version of gcc are you running?
- On the command line you can use the following
- gcc –version – first line shows the compiler version
- gcc -v – more info (including threading model, configuration and
- Or you can use your package management utilities to determine the version of the gcc package
- In your source code (TODO)

---
What version of gcc are you running?
- In your source code you can use the following macros
- __VERSION__ - has the compiler version you are using as a string
- __GXX_ABI_VERSION – has the C++ ABI version that the current compiler implements
- linux, __linux, __linux__, unix, __unix, __unix__, __gnu_linux__ are defined symbols

---
What version of gcc are you running? (cont)
- __GNUC__ - is your compilers major version number
- __GNUC_MINOR__ - has the minor version of your compiler
- __GNUC_PATCHLEVEL__ - has the patch level of your compiler

---
The preprocessor
- cpp on the command line
- echo | g[cc|++] -E -dM - - will dump your preprocessors defined symbols for C